- المواصفات الفنية وعناصر الإسناد الفني لحافلات (51) راكب عدد (71):

| Requirements | S.N | System |
| --- | --- | --- |
| Not less than 51. | 1 | Seating Capacity |
| Diesel. | 2 | Engine |
| 4 strokes, 6-cylinder, turbo charged, direct injection, water-cooled. | 3 |  |
| Not less than 420 hp | 4 |  |
| According to euro standards: euro 5. | 5 | Fuel Specifications (emission rating) |
| Manual Shift, With At Least 6 Speeds Forward and One Reverse Speed. | 6 | Gear box |
| Not less than (600) liter capacity. | 7 | Fuel Tank (s) |
| Lockable with key. | 8 |  |
| The Fuel Filler Cap or a Location Near the Fuel Filler Cap Shall Be Labeled, With the Type of Fuels Compatible with The Vehicle. | 9 |  |
| Air suspension system. | 10 | Suspension System |
| Full Air Dual Independent Front and Rear Circuit. | 11 | Braking System |
| Abs. | 12 |  |
| Asr. | 13 |  |
| Hill holder (front & rear). | 14 |  |
| With retarder, hydraulic. | 15 |  |
| Not More Than One Manufacturing Year Life (since delivery date) for All Tires Including Spare. | 16 | Tires |
| Lift hand drive (LHD). | 17 | Steering |
| Fully powered. | 18 |  |
| Adjustable. | 19 |  |
| White. | 20 | Paint Type |
| Well Known, Reliable with High Quality, From Dependable Countries Using Such Type of Vehicles. | 21 | Origin |
| 2023 Model Year or Later. | 22 | Manufacturing year |
| Driver resting area with bed. | 23 | Additional Requirements |
| Passenger's lavatory. | 24 |  |
| Lockable luggage compartments, identically keyed. | 25 |  |
| Automatic Fire Suppression System for Engine Compartment With In-Cab Monitoring Alarm. | 26 |  |
| Safety hammers, Qty. (6) at least. | 27 |  |
| Spare Wheel with Holder or Any Other Type of Mounting. | 28 |  |
| BII (Basic Issue Items) To Include but Not Limited To: General Mechanics Tool Kit, Tire Changing Tool, Lifting Jack, Tire Inflating Hose of Sufficient Length to Inflate All Tires on Vehicle, Chuck, Pressure Gauge, First-Aid Kit, Red Emergency Reflective Triangles, Lubricating Guns. | 29 |  |
| Main circuit breaker. | 30 |  |
| Mud guards. | 31 |  |
| Front pintle hook. | 32 |  |
| Two Roof Hatches with Ventilation Vanes. | 33 |  |
| Central Air Conditioning System (Cooling and Heating) To Cover All the Cab. | 34 |  |
| Digital tachometer, with Speed Limit program. | 35 |  |
| On board diagnostic system. | 36 |  |
| Heated Front, Side (electrical) and Blind Spot Mirrors. | 37 |  |
| All Windows and Windshield To Be Double Glazed and 30% Tinted. | 38 |  |
| Driver’s Suspension Seat with Head Rests, Arm Rests, Front Sunvisor, Seat Belts and USB Charging Ports. | 39 |  |
| Passengers Luxury, High Back, Adjustable Seats With: Head Rests, Arm Rests, Foot Rest, Seat Belts and USB Charging Ports. | 40 |  |
| Frontal and Rear Fog Lights. | 41 |  |
| Two passenger's access doors. | 42 |  |
| Radio/ CD Player/ Two LED screen. | 43 |  |
| Passenger's addressing system with microphone. | 44 |  |
| Mounted GPS device. | 45 |  |
| Reverse Warning Lights and Buzzer. | 46 |  |
| Overhead storage area. | 47 |  |
| Two onboard fridges. | 48 |  |
| Rear View Camera with Display at Dashboard. | 49 |  |
| Operator manual, one copy with each vehicle. | 50 | Technical Support Requirements |
| Spare Parts and Workshop Manuals Up to Overhaul Level (Hard or Soft Copies). | 51 |  |
| Engine and Transmission Performance Sheets. | 52 |  |
| Technical Document Showing Preventive Maintenance Checks and Services. | 53 |  |
| Account For JAF On ONLINE Portals to Get Access to The Technical Manuals of All Vehicle's Components and Systems. | 54 |  |
| List of Available Special Tools Up to Overhaul Level. | 55 |  |
| Recommended Spare Parts List (10% Of Vehicle's Value) For JAF Review and Selection to Include, But Not Limited To: Fast moving Items. Fuel Injectors. Filters, Cleaners and Preventive Maintenance Requirements. Engine Qty (1), Transmission Qty (1), Generator Qty (2), Starter Motor Qty (2), Fuel Pump Qty (2), Front Axle Qty (2), Rear Axles Qty (2), Turbocharger Qty (2), radiator Qty (2). | 56 |  |
| Commitment From the Vendor to Supply Spare Parts for a Period Not Less Than 10 Years. | 57 |  |
| Diagnosis device (scan tool) qty (4). | 58 |  |
| Manufacturer warranty through local dealer for all systems and components for period not less than 2 years’ or 200,000 Km, whichever comes first. | 59 |  |
| Training: Operator. 1st + 2nd Levels Repairs. Depot Maintenance Repairs (4th Level) (Engine + Transmission). | 60 |  |
| Upon completion of manufacturing of the first batch Contractor shall conduct Factory Acceptance Test (FAT) at contractor premises. | 61 | Delivery |
| Partial delivery is allowed With first batch to be not less than (20) vehicles. | 62 |  |
| Each vendor to provide delivery timelines showing nearest date of the first batch. With preference to shortest lead-time for the whole batch (es) . | 63 |  |

- المواصفات الفنية وعناصر الإسناد الفني لحافلات الـ  (VIP) عدد (2):

- المواصفات الميكانيكية  كما هو مطلوب في حافلات الـ (51) راكب اعلاه.

- الكراسي بنظام كنب متقابل.

- وجود طاولات وسط مصممة بين الكراسي.

- سعة الحافلة (20-25) راكب.

- وجود دورة مياه مريحه.

- وجود شاشة عرض عدد (2).

- يتوفر فيها (ستائر وموكيت وثلاجة مكتب).

- الشروط الخاصة:

- يجب على الشركة بيان مدة التسليم والمخطط الزمني لتسليم كامل الكمية.

- يجيب على الشركة فصل العرض الفني في مغلف والعرض المالي في مغلف مالي منفصل.

- يجب ان تكون الشركة مسجلة بنظام الفوترة الوطني الالكتروني.

- على الشركة ارفاق كافة النشرات الفنية والكتالوجات التي تبين مطابقة الحافلات المعروضة من قبلها للمواصفات المطلوبة في دعوة العطاء.

- على الشركة ارفاق كشف مطابقة فنية للمواصفات المطلوبة في دعوة العطاء مع ضرورة بيان اية ملاحظات او اسباب في حالة عدم المطابقة او في حال كانت المواصفة المتوفرة اعلى من المواصفات المطلوبة في دعوة العطاء.

- على الشركة ارفاق التصميم الداخلي لحافلات الـ (VIP) مع العرض الفني المقدم من قبلها لتتم دراسة مدى تلبيته للاحتياج ويحق للقوات المسلحة الاردنية-الجيش العربي طلب اي تعديل على التصميم في حال تمت الاحاله على الشركة دون اي تكلفه اضافية.

- على الشركة ارفاق صورة عن شهادات الجودة وفحوصات السلامه العامة الحاصلة عليها حافلاتها.

- يجب ان يكون ارتفاع الممرات الداخليه وعرضها في الحافلات حسب المقاييس العالمية وبما يحقق حرية حركة صعود ونزول الركاب للحافلة.

- يجب على الشركة بيان صلاحية العرض المقدم من قبلها في العرضين الفني والمالي المقدمين من قبلها.

- على الشركة ارفاق نسخة الكترونية عن العرض الفني والعرض المالي في المغلف العائد لكل عرض.

- يجب ان تكون جميع النوافذ مزودة بستائر.