- Dual Sensor Thermal Network Camera:  (Qty= 6 ).

(Minimum requirement)

Pan Tilt Zoom feature

IP functionality (including control)

- Thermal Imager

- Long life Un-cooled thermal sensor

- Image size 640 x 480 or higher

- Not less than 100mm lens

- Exchangeable camera modules

- Multi Streaming

- Streaming video : MPEG, H.264 or better

- Day/Night Camera

- Not less than 30x optical zoom

- Not less than 2MP resolution

- IP66 housing

- Operating temperature: -10°C to +55°C

2.  Network Video Recorder (NVR):   (Qty= 2 ).

(Minimum requirement)

- NVR shall be support  day/night  and thermal camera .

- Not less than 16 CH with 4T HDD

- Playback and record simultaneously, without affecting recording

- Should offer two or more control levels:

    - User mode for operators to control cameras and view recordings only.

    - Administrator level for engineers for configuring and maintaining the system.

- HDMI and VGA output.

- Search mode: Date/time, Event (Motion, alarm)

- PTZ control .

- Support  live view for all cameras on high resolution (up to 5MP) .

- Streaming video : MPEG, H.264 or better.

  - Hardware Warranty for 2 years.

  - Country of origin worldwide (well known brand to SCC).