العطاء رقم م ش ع 3/ 113/ 25/ 2021

شراء رأس سحب عدد (15)

- المواصفات الفنية

| requirements | system | Ser. |
| --- | --- | --- |
| 6X4 With Differential Lock. | Configuration |  |
| 40 Ton Payload. | Load Capacity |  |
| 3.5 inch. | King Pin 5th wheel Diameter |  |
| Diesel, 4 Stroke, 6 Cylinder, Turbo Charged, Direct Injection, Water Cooled, With Fan Dust Cover and Fuel Water Separator. | Engine |  |
| According To EURO Standards (High Sulfur Content Diesel Fuel, 10000 PPM or NOT More Than EURO ӀӀӀ). | Fuel Specifications (emission rating) |  |
| Not Less Than 500 Liter Capacity. Lockable With Key. The Fuel Filler Cap or a Location Near The Fuel Filler Cap Shall Be Labeled, With The Type of Fuels Compatible With The Vehicle. | Fuel tank |  |
| Automatic or Automated Gear Shift Without Clutch Pedal, Power Shift Transmission. | Gear box |  |
| Leaf Springs With Shock Absorber. | Suspension System |  |
| Full Air Dual Independent Trailer Brake: ABS + Hill Holder (Front And Rear) With Retarder + TCS + Trailer Handbrake. | Braking System |  |
| Sleeper Cab. | Cab |  |
| On/Off Road, not More Than 1 Manufacturing Year Life for All tires Including Spare.. | Tires |  |
| Lift Hand Drive (LHD), Fully Powered, Adjustable | Steering |  |
| Japan, Europe Or USA. | Origin |  |
| The Vehicle Shall Be A 2021 Model Year Or Later. | Manufacturing year |  |
| 12 Or 24 Volt, Adapter For Power Supply The Trailer (15 Pin To 2*7 Pin Socket) For 12 Volt Electrical System Tractor Head, It Should Supply 24 Volt To Semitrailer. | Electrical System |  |
| - Spare Wheel With Holder. - BII (Basic Issue Items) To Include But Not Limited To: General Mechanics Tool Kit, Tire Changing Tool, Lifting Jack, Tire Inflating Hose With Quick-Connect Fitting On Both Ends Powered By Vehicle Compressed Air System of Sufficient Length To Inflate All Tires On Vehicle With Chuck And Pressure Gauge, Fire Extinguisher With Mounting Bracket, Three Red Emergency Reflective Triangles. - A Metal Ladder To Aid Crew Ingress/Egress Into The Rear of Cab. - Wheels Shall Be With Mud Guards. - (2) Front And Two (2) Rear Frame Mounted Hooks. - Front And Rear Pintle Hooks. - Two Lockable Toolboxes, Identically Keyed. - Air Conditioning System (Cooling and Heating) To Cover All The Cab (Driver And Sleeper). - Rear and Front Fog Defrosters. - Switch, Battery, Disconnect. - Speed Limiter. - On Board Diagnosis - Heated Front, Side and Blind Spot Mirrors. - Power Windows For Driver And Co-Driver. - Axle Load Measuring Device. - Driver’s Suspension Seat. - Driver And Co-Driver: Head Rests, Hand Rests, Front Sunvisor and Seat Belts. - Frontal Fog Lights. - Reverse Warning Lights and Buzzer. - Tail Lights Guard. - Metallic Bumpers and Corners. | Additional Requirements |  |

- الشروط الخاصة:

1. على الشركة توضيح كل مواصفة من مواصفات العطاء بعرضها وارفاق ما يثبت (كتالوجات وعرض الشركة) بأن المواصفة متوفرة بالالية المقدمة على شكل COMPLIANCE SHEET  مع ذكر رقم الصفحة بالكتالوج او العرض مقابل كل مواصفة من مواصفات العطاء ولن يقبل أي عرض لا يتضمن COMPLIANCE SHEET  .

2. يضمن مع عرض السعر قطع غيار احتياطية بقيمة (10%) من ثمن الالية ويتم التنسيق عليها بعد الاحالة.

3. يتم تضمين عناصر الاسناد الفني التالية عند الاحالة :

أ. التدريب الفني لدى الشركة الموردة ولغاية مستوى الافرهول.

ب.الضمان لمدة لا تقل عن سنة.

جـ. الصيانة المجانية وحسب تعليمات الشركة الصانعة.

د. الكتالوجات الفنية (مستخدم، قطع غيار لمستوى الافرهول، تصليحات فنية لمستوى الافرهول).