العطاء رقم م ش ع 3/ 112/ 24/ 2021

شراء الية شحن حمولة (10-15) طن عدد (10)

المواصفات الفنية لآلية شحن (10-15) طن

| requirements | system | Ser. |
| --- | --- | --- |
| 10-15 Ton. | Load Capacity |  |
| Diesel, 4 Stroke, 6 Cylinder, Turbo Charged, Direct Injection, Water Cooled, With Fan Dust Cover and Fuel Water Separator. | Engine |  |
| According To EURO Standards (High Sulfur Content Diesel Fuel, 10000 PPM or NOT More Than EURO ӀӀӀ). | Fuel Specifications (emission rating) |  |
| Not Less Than 500 Liter Capacity. Lockable With Key. The Fuel Filler Cap or a Location Near The Fuel Filler Cap Shall Be Labeled, With The Type of Fuels Compatible With The Vehicle. | Fuel tank |  |
| Automatic or Automated Gear Shift Without Clutch Pedal, Power Shift Transmission. | Gear box |  |
| Leaf Springs With Shock Absorber. | Suspension System |  |
| Full Air Dual Independent Trailer Brake: ABS + Hill Holder (Front And Rear) With Retarder + TCS + Trailer Handbrake. | Braking System |  |
| Sleeper Cab. | Cab |  |
| On/Off Road, not More Than 1 Manufacturing Year Life for All tires Including Spare.. | Tires |  |
| Lift Hand Drive (LHD), Fully Powered, Adjustable | Steering |  |
| Japan, Europe Or USA. | Origin |  |
| The Vehicle Shall Be A 2021 Model Year Or Later. | Manufacturing year |  |
| 12 Or 24 Volt. | Electrical System |  |
| - Spare Wheel With Holder. - BII (Basic Issue Items) To Include But Not Limited To: General Mechanics Tool Kit, Tire Changing Tool, Lifting Jack, Tire Inflating Hose With Quick-Connect Fitting On Both Ends Powered By Vehicle Compressed Air System of Sufficient Length To Inflate All Tires On Vehicle With Chuck And Pressure Gauge, Fire Extinguisher With Mounting Bracket, Three Red Emergency Reflective Triangles, Towing Cable/Strap At Least 8 Meters Long. - Removable Weather Resistant Soft Cover and Support Structure For The Cargo Body With Required Straps. - A Metal Ladder To Aid Crew Ingress/Egress Into Rear Cargo Body and The Rear of The Cab. - Wheels Shall Be With Mud Guards. - (2) Front And Two (2) Rear Frame Mounted Hooks. - Front And Rear Pintle Hooks. - Two Lockable Toolboxes, Identically Keyed. - Side Water Tank, Not Less Than 100 liters Capacity. - Air Conditioning System (Cooling and Heating) To Cover All The Cab (Driver And Sleeper). - Rear and Front Fog Defrosters. - Switch, Battery, Disconnect. - Speed Limiter. - On Board Diagnosis - Heated Front, Side and Blind Spot Mirrors. - Power Windows For Driver And Co-Driver. - Axle Load Measuring Device. - Driver’s Suspension Seat. - Driver And Co-Driver: Head Rests, Hand Rests, Front Sunvisor and Seat Belts. - Frontal Fog Lights. - Reverse Warning Lights and Buzzer. - Tail Lights Guard. - Metallic Bumpers and Corners. | Additional Requirements |  |

صندوق حمولة (مفتوح) لآلية شحن (10-15) طن

أ.	المقاسات والأبعاد. تحدد حسب نوع الالية المشتراة.

ب.	الشاصي. شاصي صندوق الحمولة يتكون من شاصي طويل على شكل (U) 14سم ويفصل بينه وبين شاصي الآلية خشب زان بسماكة 15سم ويكون الخشب قطعة واحدة متصلة ، يتم تثبيت شاصي صندوق الحمولة مع الخشب مع شاصي الآلية الرئيسي بواسطة بندات ذات توزيع مناسبة (لا تزيد المسافة بين البندة والأخرى عن 80 سم) ويجب تثبيت البندات بطريقة لا تسمح لصندوق الحمولة بالانزلاق الجانبي والأمامي والخلفي.

جـ.	الأرضية. أرضية الصندوق مغطاة بخشب لاتيه سماكته لا تقل عن 20 ملم ومغطى من الأعلى والأسفل بصاج حديد مبزر سماكة لا تقل عن 4 ملم ، والأرضية مقواة من الأسفل بعوارض معدنية على شكل (U) وموزعة على طول الأرضية بحيث تكون المسافة بين كل عارضتين لا تزيد عن 50 سم ومزودة بشناكل لتثبيت الحمولة لا يقل عددها عن 3 لكل جهة.

د.	الحائط الأمامي. مصنوع من صفائح الحديد المضلع سماكة لا تقل عن 4 ملم وبارتفاع يغطي كامل الغرفة الأمامية.

هـ.	الباب الخلفي. قطعة واحدة من الحديد المضلع سماكة لا تقل عن 3 ملم مزودة بفصالات وأقفال تسمح بأن يفتح الباب للأسفل مع واقيات مطاطية تمنع اصطدامه بظهر الآلية.

و.	الجوانب. كل جانب لا يقل ارتفاعه عن 120 سم ويتكون من 3 قطع مصنوعة من صفائح الحديد المضلع سماكة لا تقل عن 3 ملم ومزود بفصالات وأقفال تسمح بأن تفتح للأسفل مع واقيات مطاطية تمنع اصطدامها بجوانب وإطارات الآلية، ويتم تركيب حنايا بين الجوانب المتقابلة وذلك لتثبيت الجوانب وتناسب تركيب شادر لها.

ز.	يجب أن تكون الأعمدة الجانبية الراكبة على صندوق الحمولة ومن جميع الجهات (الأمامية ، الجانبية) على شكل حرف (U) وموزعة بطريقة تمنع البضاعة من السقوط بحيث تكون المسافة بين أي عامودين لا تزيد عن (50سم) مع تثبيت ألواح خشب زان على الجزء العلوي منها (فوق الحديد المضلع) حتى اعلي صندوق الحمولة على ان لا تزيد المسافة بين ألواح الخشب عن (20سم).

ح.	توضيع شناكل بكميات كافية لتثبيت الشادر على صندوق الحمولة.

ط.	الدهان. تنظيف كافة القطع بالرمل واستخدام دهان أساس مانع للصدأ قبل الدهان النهائي.

الشروط الخاصة:

1. على الشركة توضيح كل مواصفة من مواصفات العطاء بعرضها وارفاق ما يثبت (كتالوجات وعرض الشركة) بأن المواصفة متوفرة بالالية المقدمة على شكل COMPLIANCE SHEET  مع ذكر رقم الصفحة بالكتالوج او العرض مقابل كل مواصفة من مواصفات العطاء ولن يقبل أي عرض لا يتضمن COMPLIANCE SHEET  .

2. يضمن مع عرض السعر قطع غيار احتياطية بقيمة (10%) من ثمن الالية ويتم التنسيق عليها بعد الاحالة.

3. يتم تضمين عناصر الاسناد الفني التالية عند الاحالة :

أ. التدريب الفني لدى الشركة الموردة ولغاية مستوى الافرهول.

ب.الضمان لمدة لا تقل عن سنة.

جـ. الصيانة المجانية وحسب تعليمات الشركة الصانعة.

د. الكتالوجات الفنية (مستخدم، قطع غيار لمستوى الافرهول، تصليحات فنية لمستوى الافرهول).