Quantities & Accessories

| 1 | Digital Mobile Radio (Portable) | QTY = 1700 |
| --- | --- | --- |
| 2 | Digital Mobile Radio (Mobile) | QTY = 250 |
| 3 | Digital Repeater Stations & Duplexer* & Antenna System | QTY = 40 |
| 4 | Portable Radio Leather carry case | QTY = 1000 |
| 5 | 3-wire surveillance Earpiece with transparent tube, PTT & MIC | QTY = 1300 |
| 6 | Extended Li-Ion battery (2000 mAh) | QTY = 1700 |
| 7 | Extended Standard Charger | QTY =1000 |
| 8 | Extended Standard VHF Antenna (Portable Radio) | QTY = 1300 |
| 9 | Programming Hardware & Software Kits (Portable Radio) with necessary cables | QTY = 10 |
| 10 | Programming Hardware &Software ( Mobile Station Radio & Repeater) with necessary cables | QTY = 10 |
| 11 | Maintenance Training for 5 working days (Covering All: Travelling Tickets, Accommodations, Transportations, Medical Insurance, etc… ) | (5) Persons |

* Duplexers sub bands will be assigned later but a unit price for duplexers should be given.

Digital Mobile Radio (Portable)

Technical Specifications

| General |
| --- |
| Frequency range | VHF: (136 – 174) MHz |
| Operating modes | Tier II: in accordance to ETSI standards TS 102 361_1 TS 102 361_2 TS 102 361_3 Analogue operation compatible with conventional radios |
| Channel capacity | >500 |
| Channel spacing | 12.5 kHz , 25 kHz |
| Antenna impedance | 50Ω |
| Battery capacity | ≥ 2000mAH |
| Display | LCD Alphanumeric full colored ≥4 lines |
| GPS | Embedded GPS |
| General Features | Group call, Individual call, , All call, Short Data Service, Authentication, Caller ID, Call History, Contact List (phone book), Multiple language capability(Arabic preferably) Time Display, Keypad (letters, numerical), Keypad Lock. |
| Encryption | AES 256 |
| Interoperability | Fully interoperable with any other DMR manufactures including encryption mode. |

Digital Mobile Radio (Portable)

Technical Specifications

| ENVIRONMENTAL SPECIFICATIONS |
| --- |
| Operating Temperature | - 30 °C to + 60 °C or better |
| Storage Temperature | - 40 °C to + 80 °C or better |
| IP rating | ≥ IP 57 |
| Ruggedness | Comply to MIL-STD-810 D / E / F / G |

| Transmitter |
| --- |
| Transmitting power | VHF :≥4W (adjustable) |
| Frequency Stability | ±1.5ppm or better |
| Modulation | FM 4FSK digital modulation |
| Nominal audio distortion | ≤ 3% |
| Digital vocoder type | AMBE+2 |

| Receiver |
| --- |
| Sensitivity (Analogue) | ≤ -117 dbm @12 db SINAD |
| Sensitivity (Digital) | ≤ -117 dbm @ BER 5% |
| Adjacent channel selectivity | ETSI : 60 dB at 12.5 kHz / 70 dB at 25 kHz |
| Intermodulation | ETSI: 65 dB at 12.5 / 25 kH |
| Spurious response rejection | ETSI: 70 dB at 12.5 / 25 kHz |
| Nominal audio distortion | ≤ 3% |

Digital Mobile Radio (Portable)

Technical Specifications

NOTES

1.	Each radio set should include:

a.    One rechargeable battery.

b.    One AC Charger.

c. Full band (136-174) MHz antenna/antennas, 
(a single wideband antenna is preferable) see note2, GPS integrated.

d.    One belt clip.

2.	Availability of the specification pointed as "Preferably"   gives an advantage if companies are equal in the rest of all other specifications.

3.	Fully featured DMR Tier2 minimum upgradable to Tier3, where breakdown prices of upgrading to Tier3 (HW, SW and licenses) shall be provided. Bidders shall adhere to these prices for the next (5) five coming years by delivering a certificate showing this condition.

4.	Two years warranty min.

Digital Mobile Radio (Mobile)

Technical Specifications

| General |
| --- |
| Frequency range | VHF: (136 – 174) MHz |
| Operating modes | Tier II: in accordance to ETSI standards TS 102 361_1 TS 102 361_2 TS 102 361_3 Analogue operation compatible with conventional radios |
| Channel capacity | >500 |
| Channel spacing | 12.5 kHz , 25 kHz |
| Power Supply | 12VDC Nominal |
| Antenna impedance | 50Ω |
| Display | LCD Alphanumeric full colored ≥ 4 lines |
| GPS | Embedded GPS |
| General Features | Group call, Individual call, , All call, Short Data Service, Authentication, Caller ID, Call History, Contact List (phone book), Multiple language capability(Arabic preferably) Time Display, Keypad (letters, numerical), Keypad Lock. |
| Encryption | AES 256 |
| Interoperability | Fully interoperable with any other DMR manufactures including encryption mode. |

Digital Mobile Radio (Mobile)

Technical Specifications

| ENVIRONMENTAL SPECIFICATIONS |
| --- |
| Operating Temperature | - 30 °C to + 60 °C or better |
| Storage Temperature | - 40 °C to + 80 °C or better |
| IP rating | ≥ IP 54 |
| Ruggedness | Comply to MIL-STD-810 D / E / F / G |

| Transmitter |
| --- |
| Transmitting power | VHF ≥ 45W (adjustable) |
| Frequency Stability | ±1.5 ppm or better |
| Modulation | FM 4FSK digital modulation |
| Nominal audio distortion | ≤ 3% |
| Digital vocoder type | AMBE+2 |

| Receiver |
| --- |
| Sensitivity (Analogue) | ≤ -117 dbm @12 db SINAD |
| Sensitivity (Digital) | ≤ -117 dbm @ BER 5% |
| Adjacent channel selectivity | ETSI : 60 dB at 12.5 kHz / 70 dB at 25 kHz |
| Intermodulation | ETSI: 65 dB at 12.5 / 25 kHz |
| Spurious response rejection | ETSI: 70 dB at 12.5 / 25 kHz |
| Nominal audio distortion | ≤ 3% |

Digital Mobile Radio (Mobile)

Technical Specifications

NOTES:

1. 	Each radio set should include:

a.   One Handheld microphone.

b.   One power Supply with cable.

c. Full band (136-174) MHz antenna/antennas,
(a single wideband antenna is preferable) see note2.

d.  GPS magnetic antenna (preferable to be integrated with VHF antenna).

2. 	Availability of the specification pointed as "Preferably gives an advantage if companies are equal in the rest of all other specifications.

3.	Fully featured DMR Tier2 minimum upgradable to Tier3, where breakdown prices of upgrading to Tier3 (HW, SW and licenses) shall be provided. Bidders shall adhere to these prices for the next (5) five coming years by delivering a certificate showing this condition.

4.	Two years warranty min.

Digital Repeater Stations & Duplexers

Technical Specifications

| General |
| --- |
| Frequency range | VHF: (136 – 174) MHz |
| Operating modes | Tier II: in accordance to ETSI standards TS 102 361_1 TS 102 361_2 TS 102 361_3 Analogue operation compatible with conventional radios |
| Channel capacity | >10 |
| Channel spacing | 12.5 kHz , 25 kHz |
| Antenna impedance | 50Ω |
| Power supply | 100-220VAC 12VDC Nominal |
| General Features | RJ45 Ethernet port(one minimum) IP Site Connection |

Digital Repeater Stations & Duplexers

Technical Specifications

| ENVIRONMENTAL SPECIFICATIONS |
| --- |
| Operating Temperature | - 30 °C to + 60 °C or better |
| Storage Temperature | - 40 °C to + 80 °C or better |

| Transmitter |
| --- |
| Transmitting power | ≥ 40 W |
| Frequency Stability | ±1.5 ppm or better |
| Modulation | FM 4FSK digital modulation |
| Nominal audio distortion | ≤ 3% |
| Digital vocoder type | AMBE+2 |

| Receiver |
| --- |
| Sensitivity (Analogue) | ≤-117 dbm @12 db SINAD |
| Sensitivity (Digital) | ≤-117 dbm @ BER 5% |
| Adjacent channel selectivity | ETSI : 60 dB at 12.5 kHz / 70 dB at 25 kHz |
| Intermodulation | ETSI: 65 dB at 12.5 / 25 kHz |
| Spurious response rejection | ETSI: 70 dB at 12.5 / 25 kHz |
| Nominal audio distortion | ≤ 3% |

Digital Repeater Stations & Duplexers

Technical Specifications

NOTES:

1. 	Each repeater set should include:

a.  12Vdc Charger (Backup Power Supply) with both 
(Ac & DC) Power Cables.

b.  One Duplexer:

(1)	Where Duplexer Sub Bands will be assigned later.

(2)	Duplexer RX/TX frequency spacing shall be not more than (5) MHz

c. Full band (136-174) MHz antenna/antennas, Including Ancillaries (connectors, Feeders, Feeder Grounding Kits, Cable Clips, Arrestors, Jumper Cables, etc…)

2.	Fully featured DMR Tier2 minimum upgradable to Tier3, where breakdown prices of upgrading to Tier3 (HW, SW and licenses) shall be provided. Bidders shall adhere to these prices for the next (5) five coming years by delivering a certificate showing this condition.

3.	Auto detection between Analog mode and Digital mode.

4.	Two years warranty min.

الشروط الخاصة

# 1.	يجب على الشركة بيان بلد المنشأ للمواد المعروضة.

2.	يجب بيان مدة التسليم وان أي تأخير بعد ذلك يترتب عليه غرامة مالية نسبتها(0.001) واحد بألف من قيمة المواد المتأخرة عن كل يوم تأخير.

3.	يجب أن تكون المواد جديدة 100% من إنتاج عام 2019 فما فوق وان تكون البطاريات من إنتاج ليس قبل ثلاثة أشهر من تاريخ التوريد.

4.	تتعهد الشركة بضمان المواد لمدة 24 شهرا" من تاريخ الاستلام النهائي للمواد من سوء المصنعية.

5.	تلتزم الشركة بتقديم كفالة صيانة 5% من قيمة الإحالة من تاريخ شهادة الصلاحية لمدة 24 شهر شاملاً القطع والأيدي العاملة.

6.	تقدم الأسعار على أساس واصل قيادة مستودعات اللاسلكي الرئيسية بالزرقاء معفاة من كافة الرسوم الجمركية والضريبة العامة على المبيعات وأية رسوم أو عوائد حكومية أخرى تسمح التشريعات النافذة بإعفاء القوات المسلحة الأردنية – الجيش العربي من دفعها .

7.	تلتزم الشركة بتدريب (5) مهندسين وفنيين على الاجهزة في الشركة الصانعه (DMR).

8.	تلتزم الشركة بتزويدنا بمخططات وكتب تعليمات فنية وكما يلي :

(Technical service manual (Hard copy and soft copy) for DMR

9.	يتم وضع العرض الفني (نسخة ورقية + نسخة الكترونية) في مغلف والعرض المالي (نسخة ورقية + نسخة الكترونية)  في مغلف منفصل ويرفق معه كفالة دخول عطاء بنسبة (5%) خمسه بالمائة من إجمالي العرض.

10.	تلتزم الشركة المناقصة بتقديم العرض كما هو مبين بالملحق الخاص بالمواصفات الفنية المرفق بوضوح تام وكما هو مطلوب بدعوة العطاء.

12.	استبدال فوري للقطع المتعطلة.

13.	تلتزم الشركة بتقديم الإسناد الفني مقابل الثمن إذا طلب منها ذلك بعد انتهاء فترة الضمان والصيانة المجانية.

14.	على الشركة تقديم اسعار ترقية وتطوير الاجهزه بكافة انواعها من Tier2 الى Tier3 شاملاً (المعدات, البرمجيات والرخص اللازمه) والالتزام بهذه الاسعار لمدة (5) خمس سنوات قادمه بموجب تقديم شهادة خطية موقعة ومصدقة حسب الاصول.

15.	تلتزم الشركة بتزويد القوات المسلحة الأردنية بقطع الغيار لمدة عشرة سنوات مقابل الثمن وحسب الأسعار السائدة في حينـــــــــــــــــــه.

16.	تلتزم الشركة بتقديم عينات من كافة الاجهزة المطلوبة للفحص الفني ومطابقة المواصفات الفنيه المطلوبــة  عند الطلب .